## Slide 1: TAU Performance System®
oneAPI Developer Summit at IWOCL 2021
April 26, 2021, 5:15 – 5:45pm CET/8:15am – 8:45am PT
https://www.oneapi.com/events/devcon2021iwocl/
Sameer Shende
Research Associate Professor and Director,
Performance Research Laboratory, OACISS, University of Oregon
http://tau.uoregon.edu/TAU_IWOCL21.pdf

## Slide 2: Challenges
With growing hardware complexity, it is getting harder to accurately measure and optimize the performance of our HPC and AI/ML workloads.
TAU Performance System®:
  Deliver a scalable, portable, performance evaluation toolkit for HPC and AI/ML workloads
  http://tau.uoregon.edu

## Slide 3: TAU Performance System®
Parallel performance framework and toolkit
  Supports all HPC platforms, compilers, runtime system
  Provides portable instrumentation, measurement, analysis

## Slide 4: TAU Performance System
Instrumentation
  Fortran, C++, C, UPC, Java, Python, Chapel, Spark
  Automatic instrumentation
Measurement and analysis support
  MPI, OpenSHMEM, ARMCI, PGAS, DMAPP
  pthreads, OpenMP, OMPT interface, hybrid, other thread models
  GPU: OpenCL, oneAPI DPC++/SYCL (Level Zero), OpenACC, Kokkos, RAJA
  Parallel profiling and tracing
Analysis
  Parallel profile analysis (ParaProf), data mining (PerfExplorer)
  Performance database technology (TAUdb)
  3D profile browser

## Slide 5: Application Performance Engineering using TAU
How much time is spent in each application routine and outer loops? Within loops, what is the contribution of each statement? What is the time spent in OpenMP loops? In kernels on GPUs.
How many instructions are executed in these code regions? Floating point, Level 1 and 2 data cache misses, hits, branches taken? What is the extent of vectorization for loops?
What is the memory usage of the code? When and where is memory allocated/de-allocated? Are there any memory leaks? What is the memory footprint of the application? What is the memory high water mark?
How much energy does the application use in Joules? What is the peak power usage?
What are the I/O characteristics of the code? What is the peak read and write bandwidth of individual calls, total volume?
How does the application scale? What is the efficiency, runtime breakdown of performance across different core counts?

## Slide 6: Instrumentation
Source instrumentation using a preprocessor
  Add timer start/stop calls in a copy of the source code.
  Use Program Database Toolkit (PDT) for parsing source code.
  Requires recompiling the code using TAU shell scripts (tau_cc.sh, tau_f90.sh)
  Selective instrumentation (filter file) can reduce runtime overhead and narrow instrumentation focus.
Compiler-based instrumentation
  Use system compiler to add a special flag to insert hooks at routine entry/exit.
  Requires recompiling using TAU compiler scripts (tau_cc.sh, tau_f90.sh…)
Runtime preloading of TAU’s Dynamic Shared Object (DSO)
  No need to recompile code! Use mpirun tau_exec ./app with options.
Add hooks in the code to perform measurements

## Slide 7: Profiling and Tracing
Tracing shows you when the events take place on a timeline
Profiling
Tracing
Profiling shows you how much (total) time was spent in each routine
Profiling and tracing
  Profiling shows you how much (total) time was spent in each routine
  Tracing shows you when the events take place on a timeline

## Slide 8: Instrumentation
Direct and indirect performance observation
  Instrumentation invokes performance measurement
  Direct measurement with probes
  Indirect measurement with periodic sampling or hardware performance counter overflow interrupts
  Events measure performance data, metadata, context, etc.
User-defined events
  Interval (start/stop) events to measure exclusive & inclusive duration
  Atomic events take measurements at a single point
      Measures total, samples, min/max/mean/std. deviation statistics
  Context events are atomic events with executing context
      Measures above statistics for a given calling path

## Slide 9: Inclusive vs. Exclusive Measurements
inclusive
duration
exclusive
duration
int foo()
{
int a;
a =a + 1;
bar();
a =a + 1;
return a;
}
Performance with respect to code regions
Exclusive measurements for region only
Inclusive measurements includes child regions

## Slide 10: Inclusive Measurements

## Slide 11: Exclusive Time

## Slide 12: How much data do you want?
Limited Profile
Flat Profile
Loop Profile
Callsite
Profile
Callpath Profile
Trace
O(KB)
O(TB)

## Slide 13: ParaProf Profile Browser
% paraprof

## Slide 14: ParaProf Profile Browser

## Slide 15: ParaProf 3D Profile Browser

## Slide 16: TAU – ParaProf 3D Visualization
% paraprof app.ppk
Windows -> 3D Visualization -> Bar Plot (right pane)

## Slide 17: TAU – 3D Communication Window
% export TAU_COMM_MATRIX=1; mpirun … tau_exec ./a.out
% paraprof ; Windows -> 3D Communication Matrix

## Slide 18: TAU: Intel oneAPI DPC++ on an Intel Gen12LP or DG1 GPU
% tau_exec –T level_zero,serial –l0 ./a.out

## Slide 19: TAU and Vampir [TU Dresden]: Intel oneAPI OpenCL (oneCCL)
% export TAU_TRACE=1; export TAU_TRACE_FORMAT=otf2
% mpirun –np 4 tau_exec –T level_zero,serial –opencl ./a.out

## Slide 20: Tracing: Jumpshot (ships with TAU)

## Slide 21: Tracing: Chrome Browser
% export TAU_TRACE=1
% mpirun –np 256 tau_exec ./a.out
% tau_treemerge.pl; tau_trace2json tau.trc tau.edf –chrome –ignoreatomic –o app.json
Chrome browser: chrome://tracing (Load -> app.json)
Notes: 21

## Slide 22: Performance Data Measurement
Direct via Probes
Indirect via Sampling
Exact measurement
Fine-grain control
Calls inserted into code
No code modification
Minimal effort
Relies on debug symbols (-g)
Call START(‘potential’)
// code
Call STOP(‘potential’)

## Slide 23: Sampling
Running program is periodically interrupted to take measurement
  Timer interrupt, OS signal, or HWC overflow
  Service routine examines return-address stack
  Addresses are mapped to routines using symbol table information
Statistical inference of program behavior
  Not very detailed information on highly volatile metrics
  Requires long-running applications
Works with unmodified executables
Time
main
foo(0)
foo(1)
foo(2)
int main() { int i; for (i=0; i < 3; i++) foo(i); return 0; } void foo(int i) {
if (i > 0) foo(i – 1); }
Measurement
t9
t7
t6
t5
t4
t1
t2
t3
t8

## Slide 24: Instrumentation
Measurement code is inserted such that every event of interest is captured directly
  Can be done in various ways
Advantage:
  Much more detailed information
Disadvantage:
  Processing of source-code / executable necessary
  Large relative overheads for small functions
Time
Measurement
int main() { int i; for (i=0; i < 3; i++) foo(i); return 0; } void foo(int i) { if (i > 0) foo(i – 1);
}
Time
t1
t2
t3
t4
t5
t6
t7
t8
t9
t10
t11
t12
t13
t14
main
foo(0)
foo(1)
foo(2)
Start(“main”);
Stop(“main”);
Start(“foo”);
Stop(“foo”);

## Slide 25: Using TAU’s Runtime Preloading Tool: tau_exec
Preload a wrapper that intercepts the runtime system call and substitutes with another
  MPI
  OpenMP
  POSIX I/O
  Memory allocation/deallocation routines
  Wrapper library for an external package
No modification to the binary executable!
Enable other TAU options (communication matrix, OTF2, event-based sampling)

## Slide 26: Event Based Sampling (EBS)
% mpirun -n 16 tau_exec –ebs a.out
Uninstrumented!
File: point_solver.F90
Line: 2705

## Slide 27: Event Based Sampling (EBS): QMCPack
Ran for 1066.528 seconds. Outside of MPI calls, TAU can explain 975.151 seconds out of 979.071 seconds of exclusive time using EBS!

## Slide 28: Event Based Sampling (EBS) shows statement level information
File: ibv_channel_manager.c
Line: 1018

## Slide 29: Event Based Sampling without symbol information (-g): QMCPack
Line number is 0!
~147.71 seconds are spent in
Qmcplusplus:DTD_Bconds::
computeDistances method

## Slide 30: TAU’s Support for Runtime Systems
MPI
  PMPI profiling interface
  MPI_T tools interface using performance and control variables
Pthread
  Captures time spent in routines per thread of execution
OpenMP
  OMPT tools interface to track salient OpenMP runtime events
  Opari source rewriter
  Preloading wrapper OpenMP runtime library when OMPT is not supported
OpenACC
  OpenACC instrumentation API
  Track data transfers between host and device (per-variable)
  Track time spent in kernels

## Slide 31: TAU’s Support for Runtime Systems (contd.)
OpenCL
  OpenCL profiling interface
  Track timings of kernels
Intel® OneAPI
  Level Zero
  Track time spent in kernels executing on GPU
  Track time spent in OneAPI runtime calls
Kokkos
  Kokkos profiling API
  Push/pop interface for region, kernel execution interface
Python
  Python interpreter instrumentation API
  Tracks Python routine transitions as well as Python to C transitions
Notes: Collect basic routine-level timing profile to determine where most time is being spent
Collect routine-level hardware counter data to determine types of performance problems
Collect callpath profiles to determine sequence of events causing performance problems
Conduct finer-grained profiling and/or tracing to pinpoint performance bottlenecks
  Loop-level profiling with hardware counters
  Tracing of communication operations

## Slide 32: Examples of Multi-Level Instrumentation
MPI + OpenMP
  MPI_T + PMPI + OMPT may be used to track MPI and OpenMP
MPI + pthread
  PMPI + pthread interfaces
MPI + Intel ® oneAPI DPC++/SYCL
PMPI + Level Zero interfaces
OpenCL + Python
  OpenCL + Python instrumentation interfaces
Kokkos + OpenMP
  Kokkos profiling API + OMPT to transparently track events
Kokkos + pthread + MPI
  Kokkos + pthread wrapper interposition library + PMPI layer
MPI + OpenCL
  PMPI + OpenCL profiling interfaces

## Slide 33: Kokkos
Provides abstractions for node level parallelism (X in MPI+X)
Productive, portable, and performant shared-memory programming model
Helps you create single source performance portable codes
Provides data abstractions
C++ API for expressing parallelism in your program
Aggressive compiler transformations using C++ templates
Low level code targets backends such as OpenMP, Pthread, DPC++/SYCL
Creates a problem for performance evaluation tools
Gap: performance data and higher-level abstractions
Solution: Kokkos profiling API for mapping performance data
https://kokkos.org Sandia National Laboratories, NM

## Slide 34: Kokkos API use in ExaMiniMD
pushRegion(“Comm::update_halo”)
popRegion
Kokkos::parallel_for

## Slide 35: ExaMiniMD: TAU Phase
Comm::update_halo phase in TAU ParaProf’s Thread Statistics Table

## Slide 36: TAU Execution Command (tau_exec)
Uninstrumented execution
  % mpirun -np 256 ./a.out
Track GPU operations
  % mpirun –np 256 tau_exec –l0 ./a.out
  % mpirun –np 256 tau_exec –opencl ./a.out
  % mpirun –np 256 tau_exec –openacc ./a.out
Track MPI performance
  % mpirun -np 256 tau_exec ./a.out
Track I/O, and MPI performance (MPI enabled by default)
  % mpirun -np 256 tau_exec -io ./a.out
Track OpenMP and MPI execution (using OMPT for Intel v19+ or Clang 8+)
  % export TAU_OMPT_SUPPORT_LEVEL=full;
  % mpirun –np 256 tau_exec –T ompt,v5,mpi -ompt ./a.out
Track memory operations
  % export TAU_TRACK_MEMORY_LEAKS=1
  % mpirun –np 256 tau_exec –memory_debug ./a.out (bounds check)
Use event based sampling (compile with –g)
  % mpirun –np 256 tau_exec –ebs ./a.out
  Also export TAU_METRICS=TIME,PAPI_L1_DCM… -ebs_resolution=<file | function | line>

## Slide 37: Intel Level Zero (TigerLake Gen12LP integrated CPUs or DG1)
% mpirun –np 64 tau_exec –l0 ./a.out
Time spent in GEMM kernel
Units: microseconds
Units: seconds

## Slide 38: MPI Tools Interface: PVARs and CVARs
% export TAU_TRACK_MPI_T_PVARS=1
% mpirun –np 64 tau_exec –T mpit ./a.out

## Slide 39: MPI Tools Interface: Control Variables (CVARs)

## Slide 40: MPI Tools Interface: Performance Variables (PVARs)

## Slide 41: TAU’s Runtime Environment Variables
Environment Variable | Default | Description
TAU_TRACE | 0 | Setting to 1 turns on tracing
TAU_CALLPATH | 0 | Setting to 1 turns on callpath profiling
TAU_TRACK_MEMORY_FOOTPRINT | 0 | Setting to 1 turns on tracking memory usage by sampling periodically the resident set size and high water mark of memory usage
TAU_TRACK_POWER | 0 | Tracks power usage by sampling periodically.
TAU_CALLPATH_DEPTH | 2 | Specifies depth of callpath. Setting to 0 generates no callpath or routine information, setting to 1 generates flat profile and context events have just parent information (e.g., Heap Entry: foo)
TAU_SAMPLING | 1 | Setting to 1 enables event-based sampling.
TAU_TRACK_SIGNALS | 0 | Setting to 1 generate debugging callstack info when a program crashes
TAU_COMM_MATRIX | 0 | Setting to 1 generates communication matrix display using context events
TAU_THROTTLE | 1 | Setting to 0 turns off throttling. Throttles instrumentation in lightweight routines that are called frequently
TAU_THROTTLE_NUMCALLS | 100000 | Specifies the number of calls before testing for throttling
TAU_THROTTLE_PERCALL | 10 | Specifies value in microseconds. Throttle a routine if it is called over 100000 times and takes less than 10 usec of inclusive time per call
TAU_CALLSITE | 0 | Setting to 1 enables callsite profiling that shows where an instrumented function was called. Also compatible with tracing.
TAU_PROFILE_FORMAT | Profile | Setting to “merged” generates a single file. “snapshot” generates xml format
TAU_METRICS | TIME | Setting to a comma separated list generates other metrics. (e.g., ENERGY,TIME,P_VIRTUAL_TIME,PAPI_FP_INS,PAPI_NATIVE_<event>:<subevent>)

## Slide 42: Runtime Environment Variables
Environment Variable | Default | Description
TAU_TRACE | 0 | Setting to 1 turns on tracing
TAU_TRACE_FORMAT | Default | Setting to “otf2” turns on TAU’s native OTF2 trace generation (configure with –otf=download)
TAU_EBS_UNWIND | 0 | Setting to 1 turns on unwinding the callstack during sampling (use with tau_exec –ebs or TAU_SAMPLING=1)
TAU_EBS_RESOLUTION | line | Setting to “function” or “file” changes the sampling resolution to function or file level respectively.
TAU_TRACK_LOAD | 0 | Setting to 1 tracks system load on the node
TAU_SELECT_FILE | Default | Setting to a file name, enables selective instrumentation based on exclude/include lists specified in the file.
TAU_OMPT_SUPPORT_LEVEL | basic | Setting to “full” improves resolution of OMPT TR6 regions on threads 1.. N-1. Also, “lowoverhead” option is available.
TAU_OMPT_RESOLVE_ADDRESS_EAGERLY | 1 | Setting to 1 is necessary for event based sampling to resolve addresses with OMPT. Setting to 0 allows the user to do offline address translation.

## Slide 43: Runtime Environment Variables
Environment Variable | Default | Description
TAU_TRACK_MEMORY_LEAKS | 0 | Tracks allocates that were not de-allocated (needs –optMemDbg or tau_exec –memory)
TAU_EBS_SOURCE | TIME | Allows using PAPI hardware counters for periodic interrupts for EBS (e.g., TAU_EBS_SOURCE=PAPI_TOT_INS when TAU_SAMPLING=1)
TAU_EBS_PERIOD | 100000 | Specifies the overflow count for interrupts
TAU_MEMDBG_ALLOC_MIN/MAX | 0 | Byte size minimum and maximum subject to bounds checking (used with TAU_MEMDBG_PROTECT_*)
TAU_MEMDBG_OVERHEAD | 0 | Specifies the number of bytes for TAU’s memory overhead for memory debugging.
TAU_MEMDBG_PROTECT_BELOW/ABOVE | 0 | Setting to 1 enables tracking runtime bounds checking below or above the array bounds (requires –optMemDbg while building or tau_exec –memory)
TAU_MEMDBG_ZERO_MALLOC | 0 | Setting to 1 enables tracking zero byte allocations as invalid memory allocations.
TAU_MEMDBG_PROTECT_FREE | 0 | Setting to 1 detects invalid accesses to deallocated memory that should not be referenced until it is reallocated (requires –optMemDbg or tau_exec –memory)
TAU_MEMDBG_ATTEMPT_CONTINUE | 0 | Setting to 1 allows TAU to record and continue execution when a memory error occurs at runtime.
TAU_MEMDBG_FILL_GAP | Undefined | Initial value for gap bytes
TAU_MEMDBG_ALINGMENT | Sizeof(int) | Byte alignment for memory allocations
TAU_EVENT_THRESHOLD | 0.5 | Define a threshold value (e.g., .25 is 25%) to trigger marker events for min/max

## Slide 44: TAU: Quickstart Guide
Setup:
% module load tau
Profiling with an un-instrumented application:
MPI: % mpirun -np 64 tau_exec -ebs ./a.out
MPI+OpenMP with Clang 9+: % export TAU_OMPT_SUPPORT_LEVEL=full; % mpirun -np 64 tau_exec –T ompt,v5 –ompt ./a.out
Pthread: % mpirun -np 64 tau_exec –T mpi,pthread –ebs ./a.out
Python+MPI+Sampling: % mpirun -np 64 tau_python –ebs ./a.py
Python+MPI+OpenCL: % mpirun –np 64 tau_python –opencl ./a.py
DPC++/SYCL (no MPI): % tau_exec –T level_zero,serial –l0 ./foo
Analysis: % pprof –a –m | more; % paraprof (GUI)
Tracing:
Vampir: MPI: % export TAU_TRACE=1; export TAU_TRACE_FORMAT=otf2 % mpirun -np 64 tau_exec ./a.out; vampir traces.otf2 &
Chrome: % export TAU_TRACE=1; mpirun –np 64 tau_exec ./a.out; tau_treemerge.pl;
% tau_trace2json tau.trc tau.edf –chrome –ignoreatomic –o app.json
Chrome browser: chrome://tracing (Load -> app.json)
Jumpshot: % export TAU_TRACE=1; mpirun –np 64 tau_exec ./a.out; tau_treemerge.pl;
      % tau2slog2 tau.trc tau.edf –o app.slog2; jumpshot app.slog2 &

## Slide 45: TAU contacts and links
GPU profiling and tracing: Sameer Shende sameer@cs.uoregon.edu
E4S: Sameer Shende sameer@cs.uoregon.edu
TAU Performance System®: http://tau.uoregon.edu
E4S: https://e4s.io

## Slide 46
Download TAU from U. Oregon
http://tau.uoregon.edu
https://e4s.io [TAU in Docker/Singularity containers]
for more information
Free download, open source, BSD license

## Slide 47: Performance Research Laboratory, University of Oregon, Eugene
www.uoregon.edu

## Slide 48: Support Acknowledgements
US Department of Energy (DOE)
  ANL
  Office of Science contracts, ECP
  SciDAC, LBL contracts
  LLNL-LANL-SNL ASC/NNSA contract
  Battelle, PNNL and ORNL contract
Department of Defense (DoD)
  PETTT, HPCMP
National Science Foundation (NSF)
  SI2-SSI, Glassbox
NASA
Intel
CEA, France
Partners:
  University of Oregon
  The Ohio State University
  ParaTools, Inc.
  University of Tennessee, Knoxville
  T.U. Dresden, GWT
  Jülich Supercomputing Center

## Slide 49: Acknowledgment
“This research was supported by the Exascale Computing Project (17-SC-20-SC), a collaborative effort of two U.S. Department of Energy organizations (Office of Science and the National Nuclear Security Administration) responsible for the planning and preparation of a capable exascale ecosystem, including software, applications, hardware, advanced system engineering, and early testbed platforms, in support of the nation’s exascale computing imperative.”